INSTALLATION PROCEDURE FOR AN IDE DRIVE

1. Install a 40 pin Data Cable ensuring that pin 1, which can be 
   identified by the striped edge of the cable, is closest to the 
   power connector on the drive.

2. Install a DC power cable to the back of the drive.

3. Verify the jumper configurations for Master/Slave operation
   (Note:  Master will be the bootable drive. The slave will not 
   be bootable.) Also make sure the existing C: drive is jumped
   to be the Master in a two drive system, not the only drive in 
   the system.

4. Apply power to the computer.

 4a. When memory test is complete go into your system's Standard 
     CMOS set-up.
     (Note:  There are various ways to get into CMOS set-up, 
      please refer to system's manual for instructions.)

 4b. If your system's BIOS supports a user programmable drive 
     type, program the BIOS with the default parameters of your 
     drive. If your system does not support a user programmable 
     drive type choose parameters that closely match but do not 
     exceed the drives MegaByte capacity. Escape from set-up 
     then choose write to CMOS and exit.

5. Boot from a DOS diskette that has FDISK.EXE and FORMAT.COM on 
   it. At the A> prompt type in FDISK. At the menu options select 
   option 1 to create a DOS partition. Another menu will appear 
   and from those options choose 1 to create a Primary DOS 
   partition. Select yes to make 1 large partition and it will 
   automatically become active. Then escape from FDISK.

6. At the A> prompt type in FORMAT C:/S This does a high-level 
   format on the drive and transfers the system files in order for 
   the drive to be bootable. (Note: IDE drives are low-level 
   formatted from the manufacturer and only need a high-level 
   format).

   To configure the drive as a slave drive repeat steps 1-4 and 
   proceed with steps 5a. and 6a. as follows:

 5a. At the C> prompt type in FDISK. When the menu options appear 
     select option 5 to switch to the second drive. Enter fixed 
     disk drive number 2. Then choose option 1 to create a DOS 
     partition, then select option 1 again to create a Primary DOS 
     partition or option 2 to create an Extended DOS partition.
     (Note: C and D drives will always be the Primary partitions 
     but only the Primary partition on C: will have a status of 
     active).

 6a. Proceed with a high-level format on the drive by typing FORMAT 
     D: (Note: Make sure the correct drive letter has been selected 
     for format).

7. The drive is now bootable. As a test remove the DOS diskette 
   from A and press reset to reboot the computer,  a  C> should be 
   displayed, the drive is now ready for operation.


                    Patty Barbee  01/18/94   Rev A